## Slide 1: Aliasing and Anti-Aliasing
Tu Changhe

## Slide 2: Examples of Aliasing

## Slide 3: Examples of Aliasing

## Slide 4: Examples of Aliasing

## Slide 5: Examples of Aliasing
Texture Errors
point sampling

## Slide 6: In photos too

## Slide 7: Texture Minification
Remember texture minification
Texture mapped triangle
  triangle small or far away
  many texels land in a single pixel
Point-sample the texture?
  i.e. take the texel at the center
  misses lots of detail
  causes “shimmering” or “buzzing”
  especially noticeable of object or view moves
Solution was to filter
Texture buzzing is an example of aliasing
  Filtering the texture is an example of antialiasing

## Slide 8: Small Triangles
Aliasing when triangles very small
  About the size of a pixel, or smaller
Scan conversion: point sampling
  Pixel color due to triangle that hits center of pixel
  Can miss triangles
  Can have gaps if narrow triangle misses pixel centers
  If view or object moves, can flicker as triangles cross pixel centers

## Slide 9: Jaggies
Aliasing when drawing a diagonal on a square grid:
  Stairstepping
Especially noticeable:
  high-contrast edges
  near horizontal or near vertical
  As line rotates (in 2D)
    steps change length
    corners of steps slide along the edge
    known as crawlies

## Slide 10: Moiré Patterns
Aliasing when rendering high detail regular patterns
  can see concentric curve patterns
  known as Moiré patterns
  caused by interference between pattern and pixel grid
Also in real life: hold two window screens in front of each other

## Slide 11: Strobing
Consider 30 frame-per-second animation of a spinning propeller
If the propeller is spinning at 1 rotation per second
  each frame shows propeller rotated 12 degrees more than previous
  looks OK
If the propeller is spinning at 30 rotations per second
  each image shows propeller rotated 360 degrees
  i.e. in same place as previous frame
  i.e. propeller appears to stand still
If the propeller is spinning at
  31 rotations per second: will appear to rotate slowly forwads
  29 rotations per second: will appear to rotate slowly backwards
Example of strobing problems
  temporal aliasing
  caused by point-sampling the motion in time

## Slide 12: Aliasing
These examples cover a wide range of problems…
  … but they all result from essentially the same thing
The image we are making is trying to represent a continuous signal
  The “true” image color is a function that varies with continuous X & Y (and time) values
For digital computation, our standard approach is to:
  sample the original signal at discrete points (pixel centers or texels or wherever)
  Use the samples to reconstruct a new signal, that we present to the audience
Want the audience to perceive the new signal the same as the original would be
  Unfortunately, the sampling/reconstruction process causes some data to be misrepresented
  Hence the term alias: some part of the signal masquerading as something else
Often refer to instances of problems as artifacts or aliasing artifacts
Antialiasing: trying to avoid aliasing problems. Three basic approaches:
  Modify the original data so that it won’t have properties that cause aliasing
  Use more sophisticated sampling/reconstruction techniques
  Clean up the artifacts after-the-fact

## Slide 13: Signal Analysis
Signal Analysis: the field that studies these problems in pure form
  Applies also to digital audio, electrical engineering, radio, …
  Artifacts are different, but the theory is the same
Includes a variety of mathematical and engineering methods for working with signals:
  Fourier analysis, sampling theory, filter, digital signal processing (DSP), …
Kinds of signals:
  electrical: a voltage changing over time. 1D signal: e = f(t)
  audio: sound pressure changing over time. 1D signal: a = f(t)
  computer graphics image: color changing over space. 2D signal: c=f(x,y)
  computer graphics animation: color changing over space & time. 3D signal: c=f(x,y,t)
Examples and concepts typically shown for scalar 1D signal
  but they extend to more dimensions for the signal parameters
  but they extend to more dimensions for the signal value
A signal:

## Slide 14: Sampling
Think of ideal image as perfect triangles in continuous (floating point) device space
  Then we are thinking of our image as a continuous signal
  Continuous image has infinite resolution
  Edges of triangles are perfect straight lines
To render this image onto a regular grid of pixels:
  We employ some sort of discrete sampling technique
  Examine the original continuous image and sample it onto a finite resolution grid of pixels
If signal represents the red intensity of our virtual scene along some horizontal line, the sampled version consists of a row of discreet 8 bit red values
  This is similar to what happens when a continuous analog sound signal is digitally sampled onto a CD

## Slide 15: Reconstruction
Once we have our sampled signal, we then reconstruct it
In the case of computer graphics, this reconstruction takes place as a bunch of colored pixels on a monitor
  In the case of CD audio, the reconstruction happens in a DAC (digital to analog converter) and then finally in the physical movements of the speaker itself

## Slide 16: Reconstruction Filters
Filtering or filtration happens at the reconstruction phase:
  raw sample data isn’t used as is
  real world isn’t discrete
Some filtering due to the device, medium, and observer
  Pixels of a monitor aren’t perfects squares or points of uniform color; they have some shape and distribution over space
  The human eye filters so that a grid of pixels appears to be a continuous image
  In audio, the loudspeaker has physical limitations on its movement
But we also introduce more filtering to help get the right result
  In audio, digital processing or analog circuitry
  In computer graphics, techniques such as bilinear or bicubic filtering

## Slide 17: Low Frequency Signals
Original signal
Point sampled at relatively high frequency
Reconstructed signal

## Slide 18: High Frequency Signals
Original signal
Point sampled at relatively low frequency
Reconstructed signal

## Slide 19: Regular Signals
Original repeating signal
Point sampled at relatively low frequency
Reconstructed signal repeating at incorrect frequency (result frequency aliases the original frequency)

## Slide 20: Nyquist Limit
Any signal can be considered as a sum of signals with varying frequencies
  That’s what an equalizer or spectrum display on an audio device shows
In order to correctly reconstruct a signal whose highest frequency is x:
  sampling rate must have frequency at least 2x
  This is known as the Sampling Theorem
    AKA Nyquist Sampling Theorem, AKA Nyquist-Shannon Sampling Theorem
  The 2x sampling frequency is known as the Nyquist frequency or Nyquist limit
Frequencies below the Nyquist limit come through OK
Frequencies above the Nyquist limit come through as lower-frequency aliases, mixed in with the data

## Slide 21: Nyquist Limit
In images, having high (spatial) frequencies means:
  having lots of detail
  having sharp edges
Basic way to avoid aliasing: choose sampling rate higher than Nyquist limit
  This assumes we are doing idealized sampling and reconstruction
  In practice, better to sample at least 4x
  But in practice, we don’t always know the highest frequency
  In fact, we might not have an upper limit!
    E.g. checkerboard pattern receding to the horizon in perspective
    Spatial frequency is infinite
    Must use antialiasing techniques

## Slide 22: Aliasing Problems, summary
Shimmering / Buzzing:
  Rapid pixel color changes (flickering) caused by high detail textures or high detail geometry. Ultimately due to point sampling of high frequency color changes at low frequency pixel intervals
Stairstepping / Jaggies:
  Noticeable stairstep edges on high contrast edges that are nearly horizontal or vertical. Due to point sampling of effectively infinite frequency color changes (step gradient at edge of triangle)
Moiré patterns:
  Strange swimming patterns that show up on regular patterns. Due to sampling of regular patterns on a regular pixel grid
Strobing:
  Incorrect or discontinuous motion in fast moving animated objects. Due to low frequency sampling of regular motion in regular time intervals. (temporal aliasing)

## Slide 23: Antialiasing

## Slide 24: Aliasing

## Slide 25: Increasing Resolution
Although the resulting picture looks better, the improvement comes at the price of quadrupling the memory cost, memory bandwidth, and scan-converting time.
Increasing resolution is an expensive solution that only diminishes the problem of jaggies – it does not eliminate the problem.

## Slide 26: Illustration of aliasing

## Slide 27: Unweighted Area Sampling
We think of any line as a rectangle of a desired thickness covering a portion of the grid.
We assume that a line contributes to each pixel’s intensity an amount proportional to the percentage of the pixel’s tile it covers.
We call the technique of setting intensity proportional to the amount of area covered unweighted area sampling.

## Slide 28: Weighted area sampling
Define a weight function: W(x,y),
the weight Wa of an area A is the
integral of W(x,y) in A.
I = Imax*Wa.
From Unweighted
to weighted!

## Slide 30: Sampling Filters
We could potentially use any one of several different sampling filters
Common options include the point, box, pyramid, cone, and Gaussian filters
  Different filters will perform differently in different situations,
  Best all-around sampling filters tend to be Gaussian in shape
The filters aren’t necessarily limited to cover only pixel.
  Commonly extend slightly outside, overlapping with the neighboring pixels.
  If filter covers less than the square pixel, will have problems like point sampling
Trying to strike a balance between:
  Eliminating unwanted alias frequencies (antialiasing)
  Eliminating wanted frequencies (blurring)

## Slide 31: Edge Antialiasing

## Slide 32: Pixel Coverage
Various antialiasing algorithms exist to color the pixel based on the exact area of the of the pixel that a triangle covers.
  But, without storing a lot of additional information per pixel, very hard (or impossible) to properly handle case of several triangle edges in a single pixel
  Impractical to make a coverage-based scheme compatible with z-buffering
  Can do better if triangles are sorted back to front
Coverage approaches not generally used in practice for rendering
  Still apply to things such as font filtering

## Slide 33: Supersampling
A more popular method (although less elegant) is supersampling:
  Point sample the pixel at several locations
  Combine the results into the final pixel color
By sampling more times per pixel:
  Raises the sampling rate
  Raises the frequencies we can capture
Commonly use 16 or more samples per pixel
  Requires frame buffer and z-buffer to be 16 times as large
  Requires potentially 16 times as much work to generate image
A brute-force approach
  But straightforward to implement
  Very powerful

## Slide 34: Uniform Sampling
Divide each pixel into a uniform grid of subpixels
Sample at the center of each subpixel
Generates better quality images than single point sampling
  Filters out some higher-than-one-pixel frequency data
  Nicely smooths lines and edges
But frequencies higher than Nyquist limit will still alias
  Regular high-frequency signals will have Moiré patterns

## Slide 35: Random Sampling
Supersample at several randomly located points
Breaks up repeating signals
  Eliminates Moiré patterns
  Instead of aliasing, frequencies greater than 1 pixel appear as noise in the image
Noise tends to be less objectionable to the viewer than jaggies or Moiré patterns
  The human eye is pretty good at filtering out noise
But suffers from potential clustering and gaps
  Result is not necessarily accurate
  Too much noise.

## Slide 36: Jittered Sampling
AKA stratified sampling,
Divide pixel into a grid of subpixels
  Sample each subpixel at a random location
Combines the advantages of both uniform and random sampling
  filters high frequencies
  frequencies greater than subpixel sampling rate turned into noise
Commonly used

## Slide 37: Reconstruction filter
Take average of all samples: box filter
Take weighted average of samples: other filters
  weight according to a box, cone, pyramid, Gaussian, etc…
Can apply weighting to uniform, random, or jittered supersamples
  little additional work

## Slide 38: Weighted Distribution
Jittered supersampling with Gaussian filtering does well
Because of the filter weights, some samples have more influence on the image than others
  e.g. with 16 samples, the 4 samples in the center can have higher total weight than the 12 others
But:
  We’re paying same computational price for samples that don’t contribute much
  We’re giving as much attention to the regions that don’t contribute much
Instead, adjust the distribution
  Put more samples in the areas that contribute more highly
  Get more accuracy for the same amount of work
  known as Importance Sampling

## Slide 39: Adaptive Sampling
More sophisticated option is to perform adaptive sampling
Start with a small number of samples
Analyze their statistical variation
  It the colors are all similar, we accept that we have an accurate sampling
  If the colors have a large variation, take more samples
  continue until statistical error is within acceptable tolerance
Varying amount of work per pixel
  Concentrates work where the image is “hard”
Tricky to add samples while keeping good distribution
  But possible!
  Used in practice, especially in research renderers

## Slide 40: Semi-Jittered Sampling
Can apply a unique jittering pattern for each pixel (fully jittered) or re-use the pattern for all of the pixels (semi-jittered)
Both are used in practice
Semi-jittering advantages:
  potential performance advantages
  can preselect a good distribution
  straight edges look cleaner
Semi-jittering disadvantages:
  re-admits subtle Moiré patterns
  because of semi-regularity of grid

## Slide 41: Mipmapping & Pixel Antialiasing
Mipmapping and other texture filtering techniques reduce texture aliasing problems
Combine mipmapping with pixel supersampling
  Choose mipmaps based on subpixel size
  Gets better edge-on behavior than mipmapping alone
But it’s expensive to compute shading at every supersample
Hybrid approach:
  Assume that mipmapping and filters in procedural shaders minimize aliasing at pixel scale
  Compute only a single shading sample per pixel
  Still supersample the scan-conversion and z-buffer
Gives edge antialiasing of supersampling and texture filtering of mipmapping
Doesn’t require cost of full supersampling
GPU hardware often does this:
  Requires increase framebuffer/z-buffer memory
  But doesn’t slow down performance much
  Works pretty well